## Slide 1: Generative AI for Designing Topology-Optimized Metamaterial Unit Cells
Summer 2026

## Slide 2: Basics
A unit cell is a small repeating building block, like one LEGO brick with a shape cut into it.
Tile copies of the block into a grid to build a whole sheet of material.
The shape inside the block describes how the whole sheet behaves, not just the base material.
Dense block → stiff and strong material.
Hinges and angled struts → auxetic material (flattens when pulled).
Open pores that collapse in a controlled way → energy absorber for crashes.
Hypothesis: Yes, a generative AI model can learn patterns from topology-optimized metamaterial designs and generate new candidate unit cells with useful mechanical behavior.

## Slide 3: Topology Optimization (TO)
Give a fixed space, loads, supports, and a material budget: where do you put material for best performance?
Split the region into a grid of finite elements; each gets a density from 0 (void) to 1 (solid)
SIMP method pushed gray densities toward clean 0 or 1 with a penalization factor.
Optimizer loops: solve FE problem, measure objective, compute sensitivities, update densities, repeat.
Structural TO minimizes compliance maximizes stiffness. Metamaterial TO tunes effective properties.
Pitfall 1 - slow: expensive FE solves, return for every new condition.
Pitfall 2 - local optima: the raw 0-2 problem is ill-posed and needs regularization (filters).

## Slide 4: TO Codes
Sigmund (2001), 99-line MATLAB code: original compact educational implementation. SIMP + optimality-criteria update + mesh-independency filter. Seeded the whole field.
Andreassen et al. (2011), 88-line code: the successor. ~100x faster on a 7500-element benchmark via vectorization and memory preallocation; adds a proper density filter.
A generative model trains on thousands of optimized layouts. These minimal solvers are the cheapest way to produce that training data.
Eschenauer & Olhoff (2001) review: explains why the raw problem is ill-posed and surveys micro- vs macro-structure approaches.

## Slide 5: Metamaterials
Behavior comes from architecture, not just the base material
Design one representative unit cell (RUC), then tile it. May need to repeat 5-10 times before having uniformly.
Homogenization with periodic boundary conditions compute the cell’s effective properties as if it were one smooth material.
Reachable targets: high stiffness-to-weight, tunable bulk/shear modulus, and negative Poisson’s ratio (auxetic).
DiffMat targets a full stress-strain curve; a flat plateau means steady energy absorption over a long stroke.
Tricky: the geometry-to-property link is one-to-many. Different shapes can give nearly identical behavior, so inverse design is hard.

## Slide 6: Binary Images
A 2D cell is an image on a pixel grid: black = solid, white = void. ‘Microstructure’ and ‘image’ mean the same thing.
Simple and complete, and it matches the FE mesh one-to-one (each pixel = one design variable).
Lets you reuse image AI: CNNs, U-Nets, GANs, diffusion models. This is the bridge to the AI toolbox.
Sizes: Kollmann 128x128, TopoDiff and DiffMat 64x64. DiffMat uses mirror symmetry to design just one quarter.
Raw output is grayscale, so you threshold (e.g. >= 0.5 → solid) to get a clean manufacturable shape.
Watch for floating (disconnected) material: looks fine in pixels but cannot be build and adds no strength.

## Slide 7: Generative AI Models
Encoder-decoder (U-Net, ResUNet): compress to a latent code, expand back. Kollmann maps inputs straight to one optimized layout.
GANs: generator vs discriminator. Fast (~0.06 s) but hard to train, generalize poorly, chase pixel similarity, often leave floating material.
Diffusion: add noise step by step, then learn to reverse it. Better quality, more stable, steerable.
  TopoDiff: 8x lower performance error and 11x fewer indeasible designs than TopologyGAN; cost is speed (~21.6 s/design)
Conditioning: extra input channels, cross-attention (DiffMat injects the target curve), and guidance (TopoDiff nudges toward low compliance + manufacturability).

## Slide 8: Data and Evaluation
Dataset sizes: Kollman 30,000 cells; TopoDiff 33,000 structures (plus guidance sets); DiffMat 30,000 cells.
Pixel-wise error is the wrong metric: a small pixel error can hide a large performance error.
TopoDiff scores compliance error, volume fraction error, load violation, and floating material instead
DiffMat validates with real experiments: machined 304 stainless steel cells, compression tested.
Notable: models invent shapes not in the training set that still hit the target behavior and survive real tests.

## Slide 9: Significance
TO shapes are free-form and intricate; 3D printing reproduces them at no extra cost. Before additive manufacturing, many were discarded as unbuildable.
Payoffs: lighter parts and lifetime cost savings (fuel, shipping), less material waste, smaller carbon footprint.
Solves specific problems too: avoiding resonance, managing thermal stress, controlling crash collapse.
Applications (aerospace (Airbus A380 edge rib), automotive (printed Light Rider frame), medical (lattice implants, scaffolds).
TO vs generative design: TO needs a human CAD model and returns one result; generative design removes that starting model. The AI papers sit closer to generative design.
Software: nTopology, SOLIDWORKS, Fusion 260, Creo, Altair OptiStruct, Tosca Structure.

## Slide 10: Summary
Topology optimization finds the best shape to cut into one block (the Sigmund/Andreassen codes implement this).
The block is a metamaterial unit cell; because it repeats, the shape sets the effective properties. Homogenization measures them.
Write the block as a binary image so a vision model can read and produce it.
A generative model learns from thousands of optimized blocks, then designs new ones on demand from a target property in seconds.
3D printing makes the result real, since additive manufactures handles exactly the complex shapes TO produces.